## Slide 1: Regulatory Priorities and Information Needs Linked to Exposure to Nanomaterials Second Quantifying Exposure to Engineered Nanomaterials from Manufactured Products (QEEN II) workshop 9-10 October 2018 Department of Labor

## Slide 2: Overview
Background on TSCA
New Chemicals Review Considerations
New Chemical Categories
Regulatory Determinations under TSCA
Issues with Developing a Nanomaterials Category

## Slide 3: Toxic Substances Control Act (TSCA) - An Overview
Provides basic authority for chemicals regulation in the U.S.
TSCA requires EPA to:
  Evaluate and, where appropriate, control unreasonable risk for new chemicals and new uses of certain existing chemicals
  Prioritize, evaluate and address risk for existing chemicals that present unreasonable risk to health or the environment
  Gather information on new and existing chemical substances and mixtures, including requiring testing where needed to fill data gaps
  Coordinate with other Federal agencies
Nanoscale materials are managed under TSCA; No U.S. legislation specific to nanoscale materials

## Slide 4: TSCA – Information Required to be Submitted for New Chemicals via Premanufacture Notices (PMNs)
Chemical Identity
  Includes particle size and particle size range
  Morphology or shape
Byproducts and impurities
Estimated production/import volume
Proposed uses and amounts for each use
Human exposure information
Disposal methods and estimates of releases to the environment
Existing test data in submitter’s possession or control concerning human and environmental effects
Notes: Assessing the Chemical
TSCA requires new chemical manufacturers and importers to submit only studies/data in their possession or control
  No minimum set of toxicity or fate studies are required
No test data are required to be submitted with a notification
  Predictive models/technical tools and professional judgment must be utilized by EPA to assess potential risks

## Slide 5: TSCA New Chemical Review Considerations
PMN Submission and identified conditions of use
Assessment of production, processing (formulation), and uses
Characterization
Worker exposure
Consumer exposure
Environmental exposure
General population exposure
Releases to air and water, disposal
Notes: The review of nanoscale materials is specific to the production or import and processing for the use and to the uses specified in the submission
Other uses (future uses) must be notified before the use starts
Assessing the Chemical
Evaluation of risks from new chemicals are considered throughout their product life cycle.
EPA’s focus
  Exposure to workers
  Site-specific assessment of environmental and general population exposure
  Consumer exposure
Assessing the Chemical
Is the information available to EPA sufficient to permit a reasoned evaluation of the health and environmental effects of the substance?
In the absence of sufficient information, may the substance present an unreasonable risk of injury to health or the environment?
Will the substance be produced in substantial quantities, and (a) enter the environment in substantial quantities or (b) may there be significant or substantial human exposure?

## Slide 6: Review of New Chemicals
EPA reviews ~1000 new chemical submissions annually
Statutory review period is short – 90 days
Very few submissions include data (<15%)
Reviews are typically based on structural analogues and categories

## Slide 7: New Chemical Categories
Chemical Categories are a practical way to extrapolate existing data to analyze related substances
Category evaluation supports:
  Greater weight of evidence
  Increased confidence in conclusions
  Better basis for establishing biological plausibility
Category analysis facilitates strategic testing to fill data gaps, where necessary
  Weight of evidence used for deciding on additional testing
  Defines the nature and scope of any potential testing needs

## Slide 8: Categorization of Nanomaterials
No category currently exists for nanomaterials specifically
U.S. focus is on toxicity of components
  For example, Cd
  Functionalization of coatings
  Persistence in the environment
Nanomaterials may also fit into existing chemical categories, such as “Respirable, poorly-soluble particulates”:
  Category is based on data for five different poorly-soluble particulates: silica, talc, titanium dioxide, a lithium manganese oxide, and carbon black
  Use U.S. NIOSH REL for CNT/CNF (1 ug/m3) for risk assessment
  Physico-chemical properties testing and a 90-day inhalation toxicity test (OECD TG 413+ BAL) are often necessary to evaluate potential health and environmental impacts of nano substances
Notes: 1 µg m(-3) as an 8-h time weighted average (TWA) of elemental carbon (EC) for the respirable size fraction.

## Slide 9: TSCA Determinations Under Section 5
Presents An Unreasonable Risk
Insufficient Information and May Present An Unreasonable Risk
Chemical Substance Produced In Substantial Quantities
Insufficient Information to Make A Reasoned Evaluation
Not Likely To Present An Unreasonable Risk

## Slide 10: Section 5 Review and Determination
Insufficient Info and May Present An Unreasonable Risk
As a result of the review, EPA determines that, in the absence of sufficient information to conduct a reasoned evaluation, the manufacture, processing, distribution in commerce, or use, may present an unreasonable risk of injury to health or the environment under the conditions of use.
Regulation under section 5(e): Regulation Pending the Development of Information
  Section 5(e) order
  Testing or other potentially useful information may be required

## Slide 11: Disposition
Disposition
Engineering controls
PPE (gloves, respirator –APF 50)
or Exposure Limit
No new use prior to notification
Very limited to no release to the environment
Limits on types of consumer uses
Testing
Notes: Unreasonable risk finding
  If EPA does make an unreasonable risk finding or a substantial exposure/release finding, EPA efforts focus on developing risk management options that allow the substance to go into commerce in a manner that protects health and the environment.
  Sometimes the substance will not go into commerce
  The majority of submissions on nanoscale materials are regulated
EPA has taken a number of actions to control and limit exposures, including:
  Limiting the uses of the nanoscale materials
  Requiring the use of personal protective equipment, such as respirators and impervious gloves
  Limiting environmental releases
  Requiring testing to generate health and environmental effects data
  Limiting the use to that identified in the PMN
    New uses would need to be reviewed before they could commence

## Slide 12: Testing
Testing
P-Chem Tests
Modified Ecotoxicity Testing
Pharmacokinetics
90-day inhalation study OECD TG 413+BAL and other
Notes: Unreasonable risk finding
  If EPA does make an unreasonable risk finding or a substantial exposure/release finding, EPA efforts focus on developing risk management options that allow the substance to go into commerce in a manner that protects health and the environment.
  Sometimes the substance will not go into commerce
  The majority of submissions on nanoscale materials are regulated
EPA has taken a number of actions to control and limit exposures, including:
  Limiting the uses of the nanoscale materials
  Requiring the use of personal protective equipment, such as respirators and impervious gloves
  Limiting environmental releases
  Requiring testing to generate health and environmental effects data
  Limiting the use to that identified in the PMN
    New uses would need to be reviewed before they could commence

## Slide 13: Nanomaterials under the TSCA New Chemicals Program
More than 210 new chemical notices for nanomaterials have been received since 2005
Most notices have completed EPA review, are regulated, but allowed in commerce
  Requirements to prevent human and environmental exposure (PPE, certain end uses not allowed, no release to water, etc.)
  Requirements to develop data for fate, ecotoxicity, and/or toxicity
A limited number of 5-day, 28-day, 90-day, acute, irritation, sensitization, intratracheal instillation, and genetic toxicity studies have been conducted on nanomaterials (many of which have been on CNTs)
Notes:   Some notices are reporting exemptions
  Consent Orders
  SNURs – many already published
How does this look? Since they bring up the 160 number we need to at least mention the exemption numbers.
* Submitted 122 PMNs 4 SNUNs
* Withdrawn 4 1
* Final decisions (total) 94 2
* Denied None 0
* Approved with 5(e) 0 2
* Approved with SNUR 36 0
* Approved with 5(e) and SNUR 58 0
* Drops 2 0
* In Progress 22 1
* Submitted 33 LoREXes 16 LVEs
* Withdrawn 3 0
* Final decisions (total) 30 15
* Denied 0 0
* Granted with Conditions 30 15
* In Progress 0 1

## Slide 14: Carbon Nanotubes/Fibers
EPA has received new chemical notices under TSCA on over 100 carbon nanotubes and fibers
Each CNT is considered a distinct chemical substance. Some key parameters:
  # walls
  inner diameter, outer diameter and length
  functionalization
  capped or open ended
  straight, branched, or tree structure
Production volumes have ranged from less than 100 kg scale to greater than 100,000 kg
Notes: 150 NM PMNs

## Slide 15: Challenges to Development of Chemical Category for CNTs
Nanomaterials (and specifically CNTs) are engineered to have particular properties, which is different than functional group-based chemicals (aldehydes, ethers, etc.)
  How do chemical-structural and material characterization properties correlate with physical-chemical properties?
  CNTs often do not exist as distinct species; rather the populations of the materials can consist of distinct species and agglomerates and aggregates
  A broad range of potential CNT forms may affect toxicology
Insufficient data to identify relevant properties or identify properties key to establishment of a CNT category
Unclear test methods/relevance of results

## Slide 16
Variables in the Building of a Specific MWCNT Category
Uncoated, Underivitized
Coated, Derivitized
TiO2
MWCNTs
 | Cytotoxicity | Inflammation | Pulmonary Fibrosis | Distal Organ Effects | Other
Metals |  |  |  |  | 
Aspect Ratio |  |  |  |  | 
Surface Area |  |  |  |  | 
Short –term in vivo verification
Compare to Known Subchronic NOAELs
Interpolation of New MWCNT NOAELs
Prioritize several MWCNTs for Targeted Subchronic Testing
In vitro results

## Slide 17: Environmental Fate of CNTs
The Agency has insufficient information regarding the fate and transport of CNTs, and makes the following protective assumptions when assessing CNTs
  0% removal by a Publicly Owned Treatment Works (POTW) or a Waste Water Treatment (WWT) Plant from either biodegradation or sorption for assessing releases to surface waters
  0% removal via incineration
  Rapid migration to groundwater from landfills
  High persistence in the environment
  Rapid transformation to highly dispersible chemical species via reaction with sunlight and natural organic matter

## Slide 18: Ecotoxicology
The Agency has not adopted a concentration of concern for CNTs
CNT toxicity generally reported in the 10s to 100s ppm for both water- and sediment-borne material
  Sublethal effects have been noted in rainbow trout at levels as low as 100 ppb.
The solubility of CNTs is predicted < 1 ppb, but stable dispersions may be created in the presence of natural organic matter or via functionalization (environmentally feasible)
Uptake studies in whole aquatic organisms indicate that CNT uptake is limited to ingested material
CNT functionalization, length, capping, and purity may affect ecotoxicology

## Slide 19: Environmental Risk Assessment
Development of nanomaterial-specific test guidelines are needed for more appropriate environmental hazard assessment
Furthermore, due to the transformation potential of CNTs, the Agency would likely require generation of additional data if a company wanted to release CNTs to the environment

## Slide 20: Occupational Exposure Challenges
Large agglomerates – do these break down into respirable and inhalable particles that can reach the deep lung? What metric describes the propensity to break down?
How do CNTs disperse in lung/other biological fluids? Is there relevance for measuring occupational exposures?
Occupational inhalation exposures to respirable particles are a key concern
  No consensus approach within EPA
  Highly dependent on model and assumptions
  Unclear how to interpret/utilize experimental data

## Slide 21: Physicochemical Factors in Context of Inhalation Toxicity

## Slide 22: Consumer Exposure Challenges
The following forms of CNTs may be distributed to consumers:
  completely reacted (cured);
  incorporated or embedded into a polymer matrix that itself has been completely reacted (cured);
  embedded in a permanent solid polymer form that is not intended to undergo further processing except for mechanical processing;
Potentially useful information is testing to address the stability of CNTs in composites

## Slide 23: For More Information
Reviewing New Chemicals Under TSCA:
https://www.epa.gov/reviewing-new-chemicals-under-toxic-substances-control-act-tsca
Control of Nanoscale Materials Under TSCA:
https://www.epa.gov/reviewing-new-chemicals-under-toxic-substances-control-act-tsca/control-nanoscale-materials-under
Predictive Models and Tools for Assessing Chemicals Under TSCA
https://www.epa.gov/tsca-screening-tools

## Slide 24: Thank you!
Kenneth Moss, US EPA
moss.kenneth@epa.gov