## Slide 1: Air Sampling Approaches for Engineered Nanoparticles used in the Semiconductor Industry
Michele N. Shepard, PhD, MS, CIH
QEEN II: 2​nd​ Quantifying Exposure to Engineered Nanomaterials from Manufactured Products Workshop, Washington, D.C.
October 9, 2018

## Slide 2: Workplace Exposure Assessment
Risk Characterization
Hazard Characterization
Exposure Assessment
Risk Management
Evaluate data on physiochemical properties and toxicity.
Apply the most practical method to identify and evaluate data on exposure scenarios.
Follow banding models, screening methods, other recommended approaches. Consider uncertainty.
Apply the hierarchy of controls and confirm protection. Communicate risks and controls. Periodically re-evaluate and improve.
Consider risks from engineered nanomaterials (ENMs) across the product lifecycle, applying a management system framework:
Air sampling to quantify exposures

## Slide 3: Air Sampling Approaches
Screening level to more comprehensive approaches, depending on objectives. Common metrics include:
Number
Mass
Size
*Particle surface area is a key factor in toxicity but not as commonly measured in workplace exposure assessments.
See the AIHA Fact Sheet: Nanoparticle Sampling and Analysis (2016)
Screening with direct-reading instruments
Filter-based samples: mass and composition
Electron microscopy (TEM/EDX): size, shape, number, composition
Notes: Measurement
  Validated methods lacking
  Time-resolved devices non-specific
  Electron microscopy methods resource-intensive
  Differentiation from incidental ultrafine particles
Interpretation
  Metrics and correlation to biological activity
  Comparative values limited
  Consensus lacking on size ranges to include and data analysis methods

## Slide 4: Air Sampling Challenges
Measurement
Commonly involves multiple methods/instruments
Electron microscopy methods resource-intensive
Validated methods limited
Time-resolved devices non-specific
Background characterization for number metric
Differentiation from incidental ultrafine particles
Results Interpretation
Metrics and correlation to biological activity
Consensus lacking on size ranges to include and data analysis methods
Comparative values limited
Images: TSI CPC; TSI SMPS

## Slide 5: Workplace Exposure Scenario: Semiconductor Fabrication
Chemical Mechanical Planarization (CMP)
Activity | Duration | Frequency
1.Operate bulk slurry delivery system | 0.25-1 hr | Daily/ weekly
2.Operate CMP Tool | 2-8 hrs | Daily
3.Set up CMP Tool | < 0.5 hr | Daily
4.Conduct PM on CMP Tool | 2-8 hrs | Monthly
5.Change pre-filter on CMP WWT system | ~ 0.5 hr | Monthly
6.Clean up slurry overflow or spill | < 1 hr | As needed
ENMs are used as abrasives in wafer polishing processes in semiconductor fabrication
Product formulations: typically include amorphous silica, aluminum oxide, or cerium oxide nanoparticles
Physical forms at semiconductor fabs: slurry, powder depending on site *or embedded on pad

## Slide 6: Exposure Assessment Approach used for an academic research project
Qualitative Assessments
Surface Sampling
Air Sampling
Direct-Reading Instruments
Filter-Based Samples
TEM/EDX
ICP-AES and Gravimetric
Optical Particle Counter
Condensation Particle Counter
Optical Particle Counter
Scanning Mobility Particle Sizer
ICP-AES: inductively coupled plasma - atomic emission spectroscopy. TEM/EDX: transmission electron microscopy/energy dispersive x-ray spectroscopy.
Wipe
Microvacuum
Figure: Shepard M. © 2014
Sampling approach applied in a semiconductor workplace. Air sampling approach used in Shepard and Brenner, Ann Occ Hyg, 2014 and surface sampling in Shepard and Brenner, Int J Occup Environ Health, 2014.

## Slide 7: Applicable Reference Values: Number
Benchmark levels above background exposures for biopersistent particles 1-100 nm (IFA, 2009, 2011)
  20,000 p/cc for granular ENMs with density > 6,000 kg/m3
  40,000 p/cc for granular ENMs with density < 6,000 kg/m3
20,000 p/cc above background (BSI, 2007)

## Slide 8: Applicable Reference Values: Mass
0.3 mg/m3 TWA for nanoscale titanium dioxide, for up to 10 hours (NIOSH CIB 63, 2011)
0.3 mg/m3 TWA as an upper bound categorical guideline adjusted for other poorly soluble low toxicity (PSLT) nanoparticles (Schulte et al., J Nanopart Res 2010; NIOSH CIB 63, 2011)
0.06 x Bulk OEL for insoluble, non-fibrous ENMs (BSI, Nanotechnologies-Part 2, 2007)

## Slide 9: Screening Approach used by EHS practitioners
Sampling approach currently being applied at three semiconductor manufacturing sites in the U.S.
Considerations in selecting initial assessment approach:
Materials of interest: ubiquitous (silica, alumina)
Clean environments with high degree of process control
Short duration tasks with potential for inhalation exposure
Limited budget/resources (for TEM or multiple DRI sets)
Limits of detection and instrument specifications
Instruments available for rental
No site-specific baseline data

## Slide 10: Screening Approach used by EHS practitioners
Screening Methods and Action Limits:
Number: task measurements with condensation particle counter; probe positioned in worker breathing zone
  20,000 p/cc above background
  Safety factors: measuring particles 20 to~1000 nm and comparing to reference value for particles <100 nm; non-specific
Mass: personal breathing zone task measurements with laser photometer with cyclone
  0.03 mg/m3 TWA
  Instrument lower size range: 0.1 µm
  Safety factors: set at 10% of NIOSH REL for nanoscale TiO2; measuring respirable particle mass; non-specific

## Slide 11: Progress and Future Directions
General increase in amount and quality of data from toxicology studies
Improved capability to collect, evaluate and interpret air sampling data with advances in:
  Occupational exposure limits (OELs) or banding approaches
  Method for setting OELs
  Instrumentation/sampling devices
  Guidelines for air sampling and analysis
Image credit: NIOSH. Agglomerates/aggregates of amorphous silica nanoparticles. [NIOSH Nanotechnology Field Team report to CNSE, 10.25.11]

## Slide 12: Acknowledgements and Disclaimers
For previous research in this area:
Funding provided by the US EPA STAR Fellowship FP-91730701 (2011-2014). The views expressed in this presentation are my own and have not been reviewed or endorsed by the EPA.
Exposure assessments of semiconductor applications conducted at SUNY Albany CNSE (2010-2014), with acknowledgements to Dr. Sara Brenner and group members. Funding for air and surface sampling equipment and laboratory analysis provided by the NanoHealth and Safety Center and SEMATECH.
No information presented is intended to provide consulting advice on specific scenarios or applications; any use or adaptation of this information is at the risk of the user.
This presentation is intended to share experiences and observations on air sampling methods used to assess and quantify airborne concentrations and potential workplace exposures to engineered nanoparticles, and references current guidelines and standards.

## Slide 13
Questions or comments:
Michele N. Shepard, PhD, MS, CIH
shepard@colden.com
518-490-2261